# POD

### Description
The On-Board Computer collects data from the sensors in the vehicle and logs and transmits them to a Server.
### Characteristics
Weight Pod	250g (0.55lbs)
Weight holding plate	68g (0.15lbs)
Weight Backbone	420g (0.92lbs)
Total weight	740g (1.62lbs)
Backbone power supply voltage	12-17 VDC
Power supply maximum current	1A
Power consumption (average)	4-7W

Power consumption not including peripherals
### Drawings and Dimensions

### Installation before event
Before shipping your vehicle to an event you will need to prepare it to receive the On-Board Computer.
A 31-35 mm hole in the vehicle body must be drilled before shipping your vehicle. There should be clearance of an equal size to the holding plate (153 x 100 mm and 60 mm depth) inside the vehicle’s body to allow for installation.
Required clearance inside vehicle’s body
The hole must be positioned on an area of the body that has a flat, unobstructed surrounding area of 153 x 100 mm (long edge parallel to direction of travel). See the footprint of the On-Board Computer in Figure 2 below.
The hole should be drilled such that, once mounted, the On-Board Computer Holding Plate be in a horizontal position, +/- 20°.
To avoid transmission issues or obstruction of antennae, the selected area must not be covered by any parts of the body or appendages.
### Installation at event
Gently pull the plug up through the shaft, connect it to the socket on the underside of the Pod and fasten the nut of the connector. Put the Pod onto the Holding Plate. The magnets will firmly fix device. If the Pod remains loose, check the installation of the Holding plate. The magnets must be on top of the Holding Plate.
### Basic Operation
#### Startup
Push the Start Button on top of the Pod to start the On Board Computer. The device is able to startup when the following conditions are met:
1. The Battery is fully charged and connected to the Backbone.
2. The Pod is connected to the Backbone
The system will show that it is powered on by the green LED on the Pod and the 12V and 3.3V LEDs on the Backbone.
The power for the sensors will be switched on during startup depending on the configuration.
#### Troubleshooting
30-60 seconds after the POWER LED is lit, the device checks its own state and the state of the connected sensors. The Backbone holds a configuration of the mandatory sensors. If there is a problem with the on board computer or one of the sensors one or more of the Pod LEDs will flash.
LEDs	Interpretation	Action
	Starting	Wait up to 60s
	Connecting	Wait
	Ready	Everything is working fine. Do not go on track if LEDs are not like this
	Problem with Sensor	Ensure all sensors are connected and Joulemeter is turned on
	Looking for GPS or cloud reception	Normal behaviour when indoors. Contact technical team if this is seen outdoors
	Battery low	Recharge OBC battery